## Slide 1
Op-Amps: Basics & Non-idealities
YR3-BE3-HBINST
Dept. of Bioengineering
E.M.Drakakis
Notes: Op-amp one of the most fundamental components of electronics.
What does the op-amp do?
Measure the difference between two voltages, then that difference is amplified by a large factor (105 , 106 )

## Slide 2
Do we need Analog Instrumentation
in a Digital world?
....ever thinner “analog shell” around the “digital egg”....
Notes: In SCC, we usually have amplification, filters…
Then this signal is converted to digital so it can be manipulated computationally.

## Slide 3
Glass capillary
Ag wire
Wood’s metal
Pt wire
0.2 mm
2 mm
Bioreactors
Potentiometric & Amperometric modules
Miniaturised Sensors
Bioinstrumentation Example I: A Practical Cell Culture Monitoring System
Notes: Sensor to measure ammonia in cell cultures at different locations.

## Slide 4
Bioinstrumentation Example II: Electrocorticography Instrument
Bipolar Analog ECoG Board
Unipolar Analog ECoG Board
Electrode
Input
Buffers & Amplifiers
Electrode
Input
Buffers & Amplifiers
Power Modules
Power Modules
Power Modules
Power Modules
Analog to Digital Converter
Analog to Digital Converter
Digital Isolator
Digital Isolator

## Slide 5
Bioinstrumentation Example III: Next Generation TBI Instrument:
Twin Wireless Neuroelectrochemical Monitoring
6 EcoG/Potentiometry channels
4 Amperometry channels
(2xDDC plus 2x I-to-V)
AT86RF231 radio chip
(2.45GHz; bita rate: 0.25-2Mbps)
EFM01-CESYS FPGA module
(Spartan3e – XC3S500E)
Notes: Smaller sensors cause less trauma in tissue but are more difficult to work with for us.

## Slide 6
General Purpose Op-Amp

## Slide 7
Op-Amp Packaging

## Slide 8
Breadboarding Practical Suggestions
Notes: If we use a voltmeter to measure a voltage across a part of a circuit, as the voltmeter has a high input impedance it affects the circuit.
Instead we use an oscilloscope(which also has a very high input impedance) and we do the measurements one-by-one. This way the circuit results to be much less affected by the measurements.

## Slide 9
The Ideal Op-Amp
Notes: In an ideal op-amp voltage Vout would be equal to:
Where Ad is the differential gain of the op-amp.
In an ideal op-amp voltage Vout would be equal to:
𝑉_𝑜𝑢𝑡= 𝐴_𝑑∙(𝑉_+−𝑉_− )
Where Ad is the differential gain of the op-amp.

## Slide 10
Wiring-up the Op-Amp

## Slide 11
Open-loop Op-Amp

## Slide 12
Open-loop Voltage Gain
Vout= Ed x (open loop gain)
BUT
Open loop gain is large!! (~ 10^5) =>
In “open loop” the op-amp behaves as a linear amplifier only for MINUTE
Input differential voltages which is impractical! =>
To maintain Vout between useful limits Op-Amps are used in feedback configuration
Notes: Open loop voltage gain is not very useful as linear region is limited by a narrow range of values for ∆Vin.

## Slide 13
Open-loop Operation Example
Notes: If A_ol * Ed exceeds +V or –V then V0 must stop at Vsat+ or Vsat- respectively

## Slide 14
Op-Amp Non-idealities

## Slide 15
Input Bias Current
Notes: Drift: aging and temperature component changes

## Slide 16
Effect of –ve Input Bias Current
Notes: Negative feed-back loop (figure a) will set a current off-set, known as parasitic input current(IB). Hence induces a voltage off-set as IB goes through Rf.
In the circuits in these 3 figures there is amplification, can quite easily be worked out.
When measuring voltages in this kind of circuits we can always subtract these systematic off-sets from our measurements.

## Slide 17
Effect of +ve Input Bias Current

## Slide 18
Compensation for equal input bias current values

## Slide 19
Input Offset Voltage

## Slide 20
Signal Gain vs. Input Offset Voltage Gain:
the inverting adder example
Notes: Because the inverting adder is a linear system we can use the superposition principle to analyze tis circuit by considering each voltage/current individually.

## Slide 21
Measurement of Input Offset Voltage

## Slide 22
Active Filter Basics
YR3-BE3-HBINST
Dept. of Bioengineering
E.M.Drakakis

## Slide 23
What is a Filter? What is its effect?
(fill in)

## Slide 24
Filter effect example: Conventional EEG vs. FBEEG
Notes: Filters alter information and it can be good or bad
Examples are full band EEG and conventional EEGs

## Slide 25
Biomimetic Bionic Cochlea Chip 1 Filter Example: Measured Results

## Slide 26
Bionic Cochlea Chip 2: Measured Results

## Slide 27
 | Frequency Domain Description | Intensity Dependent Parameterisation | Biomimicry
GTF |  Very Complex |  Not Easy |  Symmetric in the passband
OZGF |  Efficiently Implementable |  Single-parameter needed |  Asymmetric In the passband
Gammatone-like Filters Modelling the operation of
A Basilar Membrane Segment
Notes: OZGF = ONE ZERO GAMMATONE FILTER

## Slide 28
Basic 1st & 2nd Order Active Filters

## Slide 29
Basic Types of Filters

## Slide 30
Choosing a proper Transfer Function for given specs
Specs
A possible (not unique!)
Transfer function which
Satisfies the specs.

## Slide 31
Basic Transfer functions of Biquadratic responses
Notes: All pass filters can be used to change the phase of the signal but doesn't affect the magnitude(in passing region) or frequency.
w0 is the pole frequency

## Slide 32
Effect of Q-value upon biquadratic responses
Notes: Q: quality factor of the filter
As the Q increases poles come closer and closer to the imaginary axes and once they cross this axis, the circuit becomes an oscillator consindering non ideality of op-amp and other omponents

## Slide 33
Phase responses of biquads

## Slide 34
Basic Low-Pass Filter

## Slide 35
Derive the LP TF & the Bode Magnitude Plot

## Slide 36
Hz vs. rad/s

## Slide 37
-40 dB/Dec LP Butterworth
Notes: 2 capacitors --> 2nd order response or less and so on

## Slide 38
Derive the -40 dB/Dec LP TF

## Slide 39
A general purpose topology: derive the general transfer function
(fill in)

## Slide 40
Basic High-Pass Filters

## Slide 41
+20 & +40 db/Dec HP Filters
What do you observe when you compare with LP topologies?
Notes: To change between low pass and high pass you change capacitors for resistors and viceversa.

## Slide 42
Band-Pass Filters
B(andwidth) = fh-fl
fr= √ (fh×fl)
Q= fr/B
Notes: These are probably the most useful filters.
If we need a narrow band-pass, many problems may arise.

## Slide 43
Elementary Wideband Filter
Notes: A band pass is like a cascade (continuation) of a low-pass filter and a high pass filter.
TF of a band-pass is the product of the LP TF and the HP TF. In general TF of any cascade of devices is the product of the TF of those devices.

## Slide 44
Elementary Narrowband Filter

## Slide 45
Notch Filters
Synthesis of a Notch from a BP & an Adder
Notes: Take bandpass filtered version of initial signal and subtract if from original signal, (performed with the adder)
TF fon would end up looking something like = -[1-|BP|] Vin

## Slide 46
A Simple Phase-Shifter Circuit

## Slide 47
A bit of Basic Theory

## Slide 48
A bit of theory: The Approximation Problem
The specifications of a filter are usually given in terms of LOSS
requirements in the stopband and the passband
The APPROXIMATION PROBLEM consists of finding/defining a function of
frequency whose LOSS lies within the targeted/permitted regions
The function – obviously – needs to be realisable by means of passive
and/or active components.
The most widely used approximation functions are the
Butterworth, Chebychev, Elliptic (or Cauer) & Bessel ones.
Loss = |H(jω)|2 = |Vin(jω)/Vout(jω)|2 = 1+ |K(jω)|2 = a0+(a1 s)+(a2 s2)+….+(ansn)
The K(jω) function must be such (in other words the an coefficients must be such) that its value is close to 1 in the passband (no loss) but during the transition from the passband to the stopband its value increases (more loss) in a manner such that the filter specifications are satisfied.

## Slide 49
Loss Graphs

## Slide 50
Higher Order Filters

## Slide 51
Increasing the order of a
LP filter increases its roll-off )
Butterworth
Chebychev
Notes: Higher order means more capactiros, more capactiors means more errors as well and also more area(which would make, for example, the PCB more expensive)

## Slide 52
Effect of Filter Order on Magnitude & Phase
Notes: If phase angle ends up being equal to 180 or a factor of this will become an oscillator.
w/ high Q many tradeso off and errors come, instead cascading low Q values simple circuit and building a high Q one works better and is more robust> This is how the cochlea works for example.

## Slide 53
Loss, Delay & Step Response of 4th-order LP Butterworth

## Slide 54
Loss, Delay & Step Response of 4th-order LP Chebychev

## Slide 55
Loss, Delay & Step Response of 4th-order LP Bessel

## Slide 56
Comparative 4th-order Responses

## Slide 57
Comparative 8-pole Responses

## Slide 58
Comparative Step Responses (various orders)
Butterworth
Chebychev (1 dB-ripple)
Bessel

## Slide 59
Basic Filter Design & Realisation Flow
Specs
Selection of the “correct”
ORDER & TYPE
Of Transfer Function
based on Specs
Realisation
Of
Selected Transfer Function
Cascade Realisation
Ladder Realisation
(1)
(2)
(3a)
(3b)
Notes: Example of cascade: 11th order: 5x2nd order + 1x1st order
All arrangemetns will bring errors
It can be shown cascade is more senstitive to errors than ladder

## Slide 60
Cascaded vs. Ladder Structures

## Slide 61
-60 dB/Dec LP Butterworth by
CASCADING a -40dB/Dec response with a -20 dB/Dec

## Slide 62
3rd- order elliptic passive ladder prototype:
topology, dynamics & SFG

## Slide 63
3rd- order all-pole passive ladder prototype:
topology, dynamics, SFG & TF

## Slide 64
Cascade filters are sensitive to (small) deviations
from nominal component values

## Slide 65
Ladder filters are less sensitive to (small) deviations
from nominal component values
Ladder
Cascade

## Slide 66: Extra Slides Practical IC Filter Examples for Biosignals

## Slide 67
Performance Summary | 
Lower cut-off frequency, f1 | 25 Hz
Upper cut-off frequency, f2 | 434 Hz
Bandwidth | 409 Hz
Dynamic Range | 62 dB
Supply Voltage | 1 V
Current Consumption | 96 nA
Bandpass Filter Example
A nW-range 25-450Hz 4thth-order Bessel Gm-C Filter for PCG

## Slide 68
Power supply (V) | +/- 1
Total capacitance (pF) | 200
Notch (8th order ) attenuation(dB) | >50
Tuning range | 10Hz-1kHz
Notch-filter Example
A µW-range 8thth-order 10Hz-1KHz Sinh Filter for ECG front-ends 50/60 Hz Noise Rejection

## Slide 69
Lowpass Bessel Filter example
A 19nW 6th-order 2-20Hz Bessel Log-domain Filter